## Slide 1
Project group SS18
Development of local positioning system for a pipe-less plant

## Slide 2: Tasks for last week
RFID Tag ID
Creating a pseudo RFID Tag in the software
Sending data µController <> Computer
RFID
  Order components
  Emulator no. 1
  Emulator no. 2
Robot Scenarios
Check the LiveStream
Create Log file for camera module

## Slide 3: RFID Tag ID
64 Bit Binary ID
101010101010100011101010100100101101010101…

## Slide 4: Pseudo RFID Tag
Adding to SensorData not possible
  Predefined Protocoll from iRobot
  Software disconnects AGV
New Protocoll for RFID Data has to be defined

## Slide 5: Communication to RFID Reader
UART0
UART1
I²C / SPI

## Slide 6
Project group SS18
Development of local positioning system for a pipe-less plant

## Slide 7: Tasks
RFID
  Order components
  Emulator no. 1
  Emulator no. 2
  CAD model of the map + drawing

## Slide 8: Order
RFID-Modul with
Evaluationboard RFIDM1356 PEB
Antenna
Size: 80 x 80 mm
Additional stuff:
Adapter cable, SMA cable, power adapter, connection cable
Samples of the RFID tags (PET and paper[0,18€/each])

## Slide 9: Emulator no. 1
Cycle time [ms]
Rob speed [m/s]
Rob start and end position [x,y]
Radius reading range [10 cm]
Distance last tag <-> boarder [cm]
Distance between tags [cm]
Length or width of plant [cm]
Matlab data in Github
Emulator
RSSI [0...7]
Time stamp [ms]

## Slide 10: Emulator no. 1
Txt file

## Slide 11: Emulator no. 2
Txt file

## Slide 12: CAD model of the map + drawing
Main area
2,3 m x 2,3 m
Additional space
1,6 m x 1,1 m
Around 7 m²

## Slide 13
Project group SS18
Development of local positioning system for a pipe-less plant

## Slide 14: Robot Scenarios
Robot diameter= 33 cm
Tag range= 10.5 cm
Scenarios
  Robot Initialization (Position & Orientation)
  Blind Spots
  Robot Lost
  Conclusion Scenarios
RSSI | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Radius in mm | 105 | 100 | 95 | 90 | 80 | 60 | 50 | 40

## Slide 15: Tags Layout (1)
Blue: Tag reading Radius 10.5 cm
X: Tags
Black: Robot
Green: Reader with distance 10 cm from robot center
RSSI= 0 tag1 & 0 tag2
Tags are 20 cm far from each other
= 25 Tags
Risk of: 0.5 cm

## Slide 16: Tags Layout (2)
RSSI= 0 tag1 & 6 tag2
Tags are 15 cm far from each other
= 45 Tags
Risk of: no blind spots

## Slide 17: Possible Scenarios
Blind Spot: use the encoder to calculate the distance
Robot Lost.
  Move a distance not more than 20 cm to identify the nearest Tag, if tag not found Halt the robot, and reset the encoder once tag detected.
Initiating
  Use a tag as Station
    Center of the Robot should start and end standing at middle of Tag
  Rotate around it self to approx. initial the orientation
  Calculate the actual angle once the robot moves

## Slide 18
Project group SS18
Development of local positioning system for a pipe-less plant

## Slide 19: Tasks for last week
Check the LiveStream
Create Log file for camera module

## Slide 20: Arslan’s suggestions
POSITION UPDATE IN GUI
Reading the position is consumed by capturing pictures (around 100 ms).
Updating the position in GUI would introduce more delays.
LIVE STREAM
Live Stream not possible with USB 2.0
It is only possible to either get the current position or live stream due to the camera
Updating the position in GUI would introduce more delays.

## Slide 21: Tracking the robot
The positions of robots was saved from python to mat files but without time stamps and can be plotted in matlab.

## Slide 22: Next steps
New code- UPDATES
Connection to robot failed, while running PUTTY
Further step
Work on the connection.