## Slide 1
Project group SS18
Development of local positioning system for a pipe-less plant
Team Members: Abdulrahman Abouelkhair, Medhini Rajagopal Balamurugan, Stefan Rottstegge, Stephan Vette
Supervised by : M.Sc.Marina Rantanen Modéer, M.Sc. Afaq Ahmad
Examined by : Prof. Dr.-Ing. Sebastian Engell

## Slide 2: Team & Organisation
Stefan Rottstegge
Software
Stephan Vette
Project Leader
Simulation
Ordering Components
Abdulrahman Abouelkhair
Commnuication Software
Hardware Setup
Ordering Components
Medhini Rajagopal Balamurgan
Existing setup
Communication Software

## Slide 3: Agenda
Introduction
Motivation and Objective
Workflow and selection process
Radio-frequency identification
Simulation
Implementation
Demonstration
Conclusions and future work

## Slide 4: DYN Miniature Pipeless plant
General setup[3x4m]
4 AGVs
2 Color Stations
1 Mixing Station
1 Storage Station
Localization
1 Camera
LED pattern on AGV
Notes: + 1 slide camera ..+positoning system

## Slide 5: Project motivation
No position update during bright day-light conditions
Accuracy : 50 – 200mm & 3-8
  Precise localization in any light conditions
Range:115-450ms
  Achieve low processing time
Increased percentage error
  Ability to localize multiple robots
Fish eye lense problem
  Develop a system without space limitation
Notes: Working in all conditions

## Slide 6: Project objective
Research about alternative positioning system
Evaluate with simulation
Ultimate goal: improve positioning precision
Compare and develop practical proof of concept

## Slide 7: Project Workflow

## Slide 8: Selection Process
Triangulation Method
  Light dependant
  Limited space
Pattern Recognition
  Complex and cost intensive
Map-Based Localization
  Drawbacks of multiple ultrasonic sensors
Radio-frequency identification
  Light independent
  Not space limited
  Common concept of indoor localization

## Slide 9: RFID (Radio Frequency Identification)
Reader
RFID Tag
Radio Waves
Notes: After in depth analysis of various localization methods we ended up choosing the radio freq. idinit due to its various advantages as discussed earlier
This technology involves a reader and a tag which placed on the object needed to be tracked.
the reader is continuously sending the radio waves, and when the tag is with in the range, its sends a feedback signal to the reader.
And the reader can track multiple objects at the same time

## Slide 10: RFID System
RFID
Tags
Active
Passive
Reader
Semi-Passive
Notes: Regarding the tags it can be either
Active: which has its own power supply,
Or passive: which relies on the radio waves which come from the reader as a source of energy,
Or semi: which has power supply but for transmitting the feedback signal it relies on the signal coming from reader.
Question?: So the rate of passive is less

## Slide 11: Plant Setup & Implementation (Alternative)
Active
systems reading range is longer
System 1
Multiple readers
1 active tag on robot
Reader
Reader
Reader
Active
Tag
Notes: - Now For a plant setup based on active tags (which was one of the alternatives), the reader would be sending the feedback info obtained from the tag to a pc or software via wire/wireless connection.
- (Click) Based on the range Multiple readers have to be installed surrounding our plant while an active tag has to be on the robot.

## Slide 12: Plant Setup & Implementation (Used)
Passive
Power for the passive tag is provided by the reader
System 2
1 reader at robot
many passive tags
Reader
Tag
Tag
Tag
Tag
Notes: - coming to the plant setup involving passive tags,(Click) one single reader would be placed on the robot while multiple tags would be installed at known locations on the plant floor, and with 10cm distance between the center of each
Due to the fact that this type of setup has less power consumption, less computational efforts for localization, and less cost, we ended up choosing this setup

## Slide 13: RFID Tags
Passive tag:
  Paper type
  Cheapest 0.18€
  Does not require power supply
  Compact
Frequency of Operation:
  125 kHz to 135 kHz
  Range: 10 cm
Working Principle:
  Inductive coupling (Near field coupling)
Tag
Tag
Tag
Tag
10 cm
Notes: - The Passive rfid tag which we use is of paper type with the cheapest cost of 18 cents/per tag.
- and works based on inductive coupling.
- Each tag contains a unique identification number and It has a range of 10 cm

## Slide 14: RFID Reader - Working Principle
Microcontroller
RFID Signal Generator
Receiver / Signal Detector
Notes: Moving on to the working of the reader, it consists of 3 main parts
- (click) Generator: which generates the radio waves.
(Click) A signal detect: which receives the feedback signal from the tag
And a microcontroller to process the information from the generator and the detector

## Slide 15: RFID Tag - Working Principle
Controller
Rectifier Circuit
Memory
Transponder
Notes: Regarding the structure of the tag, it consists of:
A Transponder: (click) that receives radio waves and (Click) sends the feedback
And a rectifier circuit which stores the energy coming from the wave across the capacitor, and this energy is used as a power supply for the controller as well as the memory

## Slide 16: Inductive coupling (Near field coupling)
RFID Reader
Rectifier
Controller
Power
Load
Clock
Notes: as discussed earlier The RFID is continuously sending radio waves with particular frequency,
- In this case the reader and the tag should be close to each other.
- (Click Here) the field which is generated by the reader is used to be coupled with antenna of the tag, and bec of this mutual coupling, the voltage is induced across the coil of tag. this voltage is rectified and used as power supply for the controller.
this voltage across the coil which is also with particular frequency, is used to derive synchronization clock for the controller.

## Slide 17: Robot Hardware Setup
Robot
Controller
WiFi module
Sensors and Actuators
Serial Communication
Notes: Moving on to the hardware, I would like to start with the robot current setup
- The in built Microcontroller on the robot receives the sensors data and sends commands to the actuators via serial communication.
- While it sends the sensor data and receive commands from the PC via WiFi module
- For less complexity and more flexibility......
Question?
(RX,TX) is the process of sending and propagating an analogue or digital information signal over a physical point-to-point (wired connection)

## Slide 18: Developed Setup
Antenna
Cable
TX
RX
Antenna
Serial Communication between WiFi Module and RFID Reader
  TX/RX
WiFi TCP-IP communication
Notes: - We developed a new communication setup for the rfid to send the data from the robot to the pc in parallel to the robot setup which we saw in the previous slid.
- It contains the antenna which sends and receives the radio waves and is connected to the RFID reader via SMA cable
- While the RFID sends the read data directly to the built-in microcontroller of wifi module via serial communication
- This WiFi module sends the received data through the network
(RX,TX) is the process of sending and propagating an analogue or digital information signal over a physical point-to-point (wired connection)

## Slide 19: Hardware Setup
Notes: as we can see here the RIFD reader and the WiFi module are placed on the top of the robot

## Slide 20: Hardware Setup
Forward
Antenna
Notes: While the antenna is fixed to the base,.. so the radio waves would be in direct contact with the tags on the floor.

## Slide 21: Communication Software
Visual Studio
Receiving
Shared
Data
Network
WiFi Module
Arduino
RFID Reader
Serial Communication
Notes: Finally on the side of the communication software.
We had overwritten on the built-in microcontroller of the Wifi Module a software which we developed (Click) to have a continuous listening to all the data which been sent from the RFID reader even if there are no tags within the range.
(Click) a TCP-IP communication is stablished within the network on the WiFi module that start publishing all the data which has been received from the reader, and this communication is killed only during the robot shutdown.
(Click) While on the other side on PC (GUI) we have established the same type of communication which should be in same network, and should grapes all the data been published by WiFi module even if it sends nothing, this communication can be stopped from the GUI if needed
Moving on to the simulation it would be discussed by my college stephan
Question? TCP/IP stands for “Transmission Control Protocol / Internet Protocol”. It is basically a network protocol that defines the details of how data is sent and received through network adapters, hubs, switches, routers and other network communications hardware.

## Slide 22: Simulation + Emulator
Emulator to create artificial RFID reader data
Answer design questions in validation
Parameter:
  Size plant [1x1m]
  Robot position + properties
  Reading ranges [0-10cm]
  Distance between the tags [10cm]
  Number of measurements for each 360°turn (Init Proc)
Output: (.txt file)
  Measurement direction of robot
  Detected unique identification (UIDs)
  Related received signal strength indicator (RSSI) [0...7]

## Slide 23: Emulator
Robot center o , dimension o
Position of the antenna ,Tags *
Max reading range of the antenna --
Orientation [˚]
UID
RSSI

## Slide 24: Simulation update
Measurements: inconsistency in RSSI and distance between tag and reader
[1] RFID-Based Localization of Mobile Robots, Christof Röhrig, Daniel Heß and Frank Künemund, FH Dortmund
Notes: Order. circle

## Slide 25: Possible reasons blind spot
The field and the inductor of the tag are perpendicular
1.5 cm
Antenna
Tag

## Slide 26: Simulation results with emulated data
Used the code to estimate the initial position and orientation with the emulated data
Without inconsistence (data from paper):
  Error in X,Y-Position: 2 mm
  Error in orientation: < 1°
After the update (with blind spot):
  Error in X, Y-Position: 10 mm
  Error in orientation: 20°

## Slide 27: Software Implementation
RX
RX
TX
TX
Reader
WiFi-Module
Receiving()
Initialization()
Position()
Orientation()
MPC()
C#
C#
C#

## Slide 28: Transmitting() Receiving()
SCAN:+UID=xxxxxxxxxxxxxxxx,+RSSI=x/x

## Slide 29: Software Implementation
RX
RX
TX
TX
Reader
WiFi-Module
Receiving()
Initialization()
Position()
Orientation()
MPC()
SCAN:+UID=xxxxxxxxxxxxxxxx,+RSSI=x/x
C#
C#
C#

## Slide 30: Data Processing
Received Data via. WiFi
Filter bad readings by “-”
Split string at “OK”, ”\r”, “\n”, “SCAN+UID=“, “RSSI=“
Convert UID from hex to dec and separate from RSSI
SCAN:+UID=E00401503A5BD691,+RSSI=0/0
SCAN:-UID=E00401503A5BDAE4
SCAN:+UID=E00401503A5BD691,+RSSI=0/0
E00401503A5BD691 0/0
1681 0/0

## Slide 31: Software Implementation
RX
RX
TX
TX
Reader
WiFi-Module
Receiving()
Initialization()
Position()
Orientation()
MPC()
SCAN:+UID=E00401503A5BD691,+RSSI=0/0
1681 0/0
C#
C#
C#

## Slide 32: Initialization()
Why is a Initialization necessary?
Initialization procedure

## Slide 33: Why is an Initialization necessary?

## Slide 34: Why a 360°turn?

## Slide 35: Recording Data
 | ID1 | ID2 | ID3 | ID4 | ID5 | ID6 | ID7 | ST1 | ST2 | ST3 | ST4 | ST5 | ST6 | ST7
0° | 4 | 1 | 5 | 2 | 3 |  |  | 0 | 0 | 1 | 7 | 0 |  | 
45° | 5 | 3 |  |  |  |  |  | 2 | 3 |  |  |  |  | 
90° | 3 | 5 |  |  |  |  |  | 2 | 2 |  |  |  |  | 
135° | 9 | 8 | 6 | 5 |  |  |  | 1 | 1 | 1 | 2 |  |  | 
180° | 9 | 7 | 8 | 6 | 4 | 5 |  | 2 | 0 | 6 | 0 | 0 | 2 | 
225° | 4 | 7 | 5 | 8 |  |  |  | 0 | 2 | 3 | 3 |  |  | 
270° | 5 | 4 | 7 | 8 | 1 |  |  | 2 | 5 | 0 | 0 | 0 |  | 
315° | 2 | 4 | 1 | 5 |  |  |  | 0 | 2 | 2 | 0 |  |  | 

## Slide 36: Analyzing Initialization Array[8,14]
ID1 | ID2 | ID3 | ID4 | ID5 | ID6 | ID7 | ST1 | ST2 | ST3 | ST4 | ST5 | ST6 | ST7
4 | 1 | 5 | 2 | 3 |  |  | 0 | 0 | 1 | 7 | 0 |  | 
5 | 3 |  |  |  |  |  | 2 | 3 |  |  |  |  | 
3 | 5 |  |  |  |  |  | 2 | 2 |  |  |  |  | 
9 | 8 | 6 | 5 |  |  |  | 1 | 1 | 1 | 2 |  |  | 
9 | 7 | 8 | 6 | 4 | 5 |  | 2 | 0 | 6 | 0 | 0 | 2 | 
4 | 7 | 5 | 8 |  |  |  | 0 | 2 | 3 | 3 |  |  | 
5 | 4 | 7 | 8 | 1 |  |  | 2 | 5 | 0 | 0 | 0 |  | 
2 | 4 | 1 | 5 |  |  |  | 0 | 2 | 2 | 0 |  |  | 

## Slide 37: Software Implementation
RX
RX
TX
TX
Reader
WiFi-Module
Receiving()
Initialization()
Position()
Orientation()
MPC()
1681 0/0
Array[8,14]
SCAN:+UID=E00401503A5BD691,+RSSI=0/0
C#
C#
C#

## Slide 38: Initial position & orientation
Based on the recorded array
ID1 | ID2 | ID3 | ID4 | ID5 | ID6 | ID7 | ST1 | ST2 | ST3 | ST4 | ST5 | ST6 | ST7
4 | 1 | 5 | 2 | 3 |  |  | 0 | 0 | 1 | 7 | 0 |  | 
5 | 3 |  |  |  |  |  | 2 | 3 |  |  |  |  | 
3 | 5 |  |  |  |  |  | 2 | 2 |  |  |  |  | 
9 | 8 | 6 | 5 |  |  |  | 1 | 1 | 1 | 2 |  |  | 
9 | 7 | 8 | 6 | 4 | 5 |  | 2 | 0 | 6 | 0 | 0 | 2 | 
4 | 7 | 5 | 8 |  |  |  | 0 | 2 | 3 | 3 |  |  | 
5 | 4 | 7 | 8 | 1 |  |  | 2 | 5 | 0 | 0 | 0 |  | 
2 | 4 | 1 | 5 |  |  |  | 0 | 2 | 2 | 0 |  |  | 

## Slide 39: CorrectDistance()
RSSI | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 
Distance in [cm] | 14 | 9.75 | 9 | 8 | 7 | 6 | 3.5 | 2.75 | Max
Distance in [cm] | 5 | 5.1 | 5.3 | 5.5 | 5.8 | 4 | - | - | Middle
Distance in [cm] | - | 4.7 | 4.5 | 4.3 | 4.2 | - | - | - | Min
Mid
Max

## Slide 40: Trilateration
Using 3 defined positions + 3 radii to estimate the intersection point
Example
  7 tags found
r3
r2
r1

## Slide 41: CenterOfRobot()
The intersection can easily be computed with the help of the four coordinates
Output of the console:
x4,y4
x1,y1
x5,y5
x8,y8
x, y
1st Antenna
2nd Antenna
3rd Antenna
4th Antenna

## Slide 42: Demonstration

## Slide 43: Demonstration

## Slide 44: Conclusion
An alternative positioning system was picked
Proof of concept was evaluated
Ultimate goal: Improve positioning precision
  Light independent system was created
  Highly scalable solution was found
  Accuracy under bad light condition was improved
    Old Error: 200mm/8°New Error: 25mm/25°
  Accuracy under perfect light condition was improved
    Old Error: 50mm/3° New Error: 25mm/25°
  Processing time was improved
    Old time: 115-450ms New Time: min 90ms
Notes: Include data abt the accuracy !!

## Slide 45: Future Work
Hardware
  Use local power supply of the robot
    Include 15V to 5V converter
  Add more the TAGs on an extended plant model
  Add RFID modules to all robots
Software
  Initialization turn based on more accurate parameter than time.
    Encoders of the robot
  Delete unused camera modules in the code
  Optimize the localization algorithm

## Slide 46
Thank you for your attention!

## Slide 47: Inductive coupling (Near field coupling)
RFID Reader
Rectifier
Controller
Power
Load
Clock
Notes: So in this case the reader and tag are so close to each other. (Click Here) So the field which is generated by the reader used to be coupled with antenna of the tag, and bec of this mutual coupling, the voltage is will be get induce across the coil of tag. Then this voltage is rectified and used as power supply for the controller as well as the memory. Now as the reader is sending waves with frequency, the voltage across the coil is also with particular frequency, which is also used to derive synchronization clock for the controller.
Question?: (load modulation) So if we connect a load of this coil so the current will start flowing through this load. So if switched on and off of this load, the current will also get switched on and off, so this switching on and off called load modulation. and if switched on and off of this load according to the data which is been stored in the tag then the data can be read by the reader in form of voltage, so using the load modulation we r changing the voltage which is been generated across the reader coil. Generating modulation an carrier frequancy

## Slide 48: WiFi Module and RFID
WiFi Module
Arduino
RFID Reader
UART
Error Scan
Scan Type Correct?
OK received
End
Received Readings
Initiate Connection (115200 Baud Rate)
Start
NO
YES
YES
NO
Comigrate Type of RFID Scan
Create Empty
Scan
NO
SCAN: +/-UID = XXXXX, +RSSI = 3/4
Module Shutdown?
YES
(Good Readings) SCAN: +UID = XXXXX, +RSSI = ¾
(Bad Readings) SCAN: - UID = XXXXX, +RSSI = ¾

## Slide 49: WiFi Module To the Network
Network
WiFi Module
Arduino
RFID Reader
UART

## Slide 50: PC receiving from the network
Connect Failed
Visual Studio
Receiving
Shared
Data
Network
SCAN:+UID=E00401503A5BD691,+RSSI=0/0
WiFi Module
Arduino
RFID Reader
UART
Server
Connection
Established?
Keep Listening to the server
End
Network
Shutdown?
Save Shared data in a String
Config. IP Address & Port of Server
Start
NO
NO
YES
YES

## Slide 51: Best 3 + correct distance

## Slide 52: Mathematical background of Trilateration
d = 10
P3(i,j)
P1(0,0)
P2(d,0)
d
i
j
,

## Slide 53: Why is the Antenna not in the Middle?