## Slide 1
Project group SS18
Development of local positioning system for a pipe-less plant

## Slide 2: Task since last meeting
Current Plant Status
Ultra-sonic Sensor
  Mobile Robots projects
  Interface between C# and ROS
  Starting Position and Orientation
RFID: Check the following (weak) points
  Accuracy
  Data rate
  Real applications/projects
  Bottlenecks
  Orientation
  Prices

## Slide 3: 1. Current Plant Status
Arslan
Remote Control of the AGVs works
Camera Calibration
  Didn´t find chessboard in image no. 1 or no. 2
Livestream
Final Feb. 2015
Camera Calibration
Live Video
AGVs start driving automatically

## Slide 4: Fixing the Chessboard Pattern
-Result: Camera can still not detect the Pattern

## Slide 5: Combination of working Software
Result: Working CameraModule was not compatible with the Arslan Software.

## Slide 6: Automatically driving AGVs
Comaration failure code with woring code
  Modifing all lines which set velocity
Copy of the working Robot Module to the failure Software
Result: Robots are still driving directly after Putty configuration

## Slide 7: 2. Ultrasonic Sensor
No multi-robots projects
  They might well conflict if they are near
  Delay between transmitting each ultrasonic sensor to be different from the other robots transmitting and receiving (suggested by users)
  Slightly different angles from one another (suggested by users)

## Slide 8: Alternatives
 | Waveshare Laser | LIDAR-Lite v3 (Garmin)
Picture |  | 
Range | 1.5 m | 40 m
Resolution | 1 cm | 1 cm
Frequency | 180 KHz | 650 KHz 1000 KHz (short distance)
Applications | Not yet | Quadcopter, etc.
Price | 14 € | 130 €

## Slide 9: LIDAR-Lite v3 (Garmin)

## Slide 10: Waveshare Laser

## Slide 11: Starting Position and Orientation
Starting and Ending of each robot task at known Position and Orientation (Docks)
Random movement for each robot to localize it self between the surrounding known obstacles & Estimating the initial position
Adding unique obstacles in the plant for the robot not getting lost

## Slide 12: Worst Case Scenaio
Getting Lost
  Similar Landmarks (using Ultrasonic Sensor)
Should surround the plant with walls

## Slide 13: Interface between C# and ROS
If you are running Windows 10 (version 1703) or newer it is possible to install and use ROS through the Windows Subsystem for Linux (WSL).
ROS on Windows Installation
ROS VSCode Extension
This Visual Studio Code(VSCode) extension provides support for Robot Operating System (ROS) development.

## Slide 14: Communication
ROSCS
roscs integrates C# written programs into ROS. It only provides support for mono under linux. A Windows extension is not planned.
XMLRPC
Using XMLRPC to communicate between C++/Python ROS nodes on the Unix machine and the C# application on Windows

## Slide 15: Communication
YARP
Not simple but efficient.
Avoids bridges
C# support provided is non-native, via SWIG(Simplified Wrapper and Interface Generator)

## Slide 16: Communication
ICE
works on a very broad range of operating systems (windows, linux, osx etc.) and languages (c++, c#, java etc.)
shares with ROS the feature, that it is very easy to use and very quickly to setup(for simpler tasks)
Compared to ACE, OpenRTM and Yarp, ICE is definitely the easiest and performance-wise strongest choice.
Simple

## Slide 17: 3. RIFD: Accuracy
Approach with SAW (surface acoustic wave) Compressive Receivers (ToA and PoA)
For an SNR (signal-to-noise-ratio) above 10 dB
MPE below 1.5%

## Slide 18: Accuracy
Active ultra-wideband (UWB) systems can tell you the location of a tagged asset to within a few centimeters. (RFID journal, http://www.rfidjournal.com/blogs/experts/entry?11454)

## Slide 19: Data rate and others
Complicated.
Information differ from 90 ms (project FH Dortmund) to a couple of seconds
No problem with the reading of multiple tags at once. Most readers have an anti-collision

## Slide 20: Real Project System 1

## Slide 21: Real Project System 1
UHF RFID ANTENNA
860-960 MHz
4.5m range

## Slide 22: Real Project System 1
SIMULTANEOUS UHF RFID READER
Simultaneous Tag reading
150 Tags per second
Connection via. USB
Aduino compatible
Signal strength available

## Slide 23: Real Project System 1
UHF RFID TAG - ADHESIVE
Can be sticked to any material
Read and Write
Truly unique ID (TID)

## Slide 24: Real Project System 1
1 x 1,50 € = 1,50€
3 x 34,95 € = 104,85€
3 x 199,95 € = 599,85€
706,20€
UHF RFID ANTENNA
RFID READER
UHF RFID TAG

## Slide 25: Bottleneck
3 Reader 1 Tag
Antenna can read 150 Tags per second.
Estimated bottleneck will be the Computation of the data send via USB

## Slide 26: Real project system 2
FH Dortmund RFID-Based Localization of Mobile Robots Using the Received Signal Strength Indicator of Detected Tags
Passive tags on the floor, one reader on the robot
Adv: Accuracy is better (detection area is smaller)
+ no reflection problems in a smaller detection area)
Combine with geometry
  RMSE around 30 mm
Drawback:
Data on the robot.
Has to send to the PC

## Slide 27: Real project system 2
One Reader per Robot = 4 x 150€ = 600€
9 Tags per m² = 9 x 10m² x 0,2€ = 18€
Total price: 618€

## Slide 28: Bottleneck
1 Reader many Tags
Computation on Aduino

## Slide 29: Orientation
Initial Turn of 90° clowise

## Slide 30: Orientation

## Slide 31: ZiggBee & RFID
ZiggBee: 2,40GHz – 2,48GHz
RFID: 860 MHz – 960 MHz
Conclusion: ZiggBee and RFID Frequenzies don´t disturbe each other.

## Slide 32: Worst Case Scenaio
Reflection of RFID signal at Metallic objects
High noise at the Metallic Stations
Wrong location near Metall

## Slide 33: Which Localization Method